## Slide 1
Module 3: Storage and Handling of the Hexavalent Vaccine

## Slide 2: Objectives
At the end of this module, you should be able to:
  Recognize the vials for the 1 dose and the 10-dose hexavalent vaccine
  Describe the correct temperature range for storing hexavalent vaccine
  Describe effects of heat exposure on hexavalent vaccine
  Understand how to check and interpret the VVM
  Understand how to handle hexavalent vaccine after opening the vial
Duration
  30’

## Slide 3: Hexavalent vaccine
Hexavalent vaccine is a ready-to-use, combination injectable vaccine in a liquid formulation
Hexavalent comes in single dose (0.5 mL) or 10-dose (5 mL) liquid vaccine vials
1 dose (0.5 mL)
10 dose (5 mL)
 | Route of administration | Shelf-life | Storage temperature | Cold chain volume per dose | Preservative | Multidose vial policy applicable
1-dose vial* | Intramuscular | 24 months | 2-8oC | 14.06 cm3 | 2-phenoxyethanol | NA (single dose)
10-dose vial | Intramuscular | 24 months | 2-8oC | 2.11 cm3 | 2-phenoxyethanol | yes

## Slide 4: At what temperature to store Hexavalent?
Hexavalent should be stored between +2° to +8° Celsius. Shelf life at this temperature is 24 months
Liquid vaccines must not be frozen and must be discarded if frozen
  If frozen, they lose their potency and provide no protection against disease
  Vaccines that have been previously frozen may also cause “aseptic abscesses”
Notes: To the facilitator:
Explain to the participants at which temperature the vaccine should be stored.
Handling vaccines requires great care. Some vaccines are sensitive to heat and some to freezing.
Careful storage and transport conditions are needed to protect vaccines from becoming ineffective and unusable.
It is important to ensure that the vaccine is not frozen.
If vaccines are frozen, they lose their potency and they would not provide adequate protection against the disease. Previously frozen vaccines may also cause "aseptic abscesses."
If frozen, DISCARD.

## Slide 5: Avoiding heat exposure of vaccine
Exposure to too much heat can also reduce the potency of the vaccine
  Protect the vaccine from too much heat and sun exposure
Hexavalent 1 and 10-dose vials will come with Vaccine Vial Monitor (VVM) on the cap and on the vial label, respectively
  The VVM records the cumulative heat exposure over time
10 dose (5 mL)
1 dose (0.5 mL)

## Slide 6: How to check and interpret the Vaccine Vial Monitor (VVM)
Before administering the vaccine, you need to check the Vaccine Vial Monitor (VVM) on the vaccine vial cap or label

## Slide 7: Vaccine Expiry Date
Remember, the VVM does not tell us everything about the potency of a vaccine:
  The VVM may be correct (the inner square lighter than outer circle), BUT the vaccine may be beyond expiry date
  Always check the expiry date on the vaccine vial label before using it

## Slide 8: Hexavalent Storage in Front-opening Refrigerators
In front-opening refrigerators, freeze-sensitive vaccines, including the hexavalent vaccine, must be placed on the middle shelf, as far as possible from the freezing compartment on top, and from the icepacks on the bottom shelf
Vials with shorter expiry dates must be stored at the front
Vials that have been exposed to heat, but VVM has not yet expired, must be placed in “use first” boxes

## Slide 9: Hexavalent Storage in Top-opening Refrigerators
In top-opening refrigerators without baskets, freeze-sensitive vaccines, including the hexavalent vaccine, must be placed as far as possible from colder zones (evaporator, bottom and walls of the unit)

## Slide 10: Hexavalent Storage in Top-opening Refrigerators
In top-opening refrigerators with baskets, freeze-sensitive vaccines, including the hexavalent vaccine, must be placed as far as possible from colder zones (bottom of the unit), and not be in contact with the walls/liner

## Slide 11: Question to Participants
Where would you store which vial in a front-opening refrigerator?
1
2
3
4
Notes: Note to facilitators:
Vial #1 should be stored behind vial # 2 to be used after vial #2 as the VVM has started to change colour.
Vial #2 should be stored at the front to be used first as it has already been opened.
Vial #3 should be stored behind vial #1 to be used after vials #1 and #2 as the VVM is still unchanged, and it has not been opened.
Vial #4 should be discarded as the VVM has gone beyond the discard point.

## Slide 12
Hexavalent – Handling the Vial after Opening
Hexavalent vaccine contains a preservative, allowing 10 dose vials to be opened and kept for use in subsequent immunization sessions for up to 28 days, provided the conditions outlined in the WHO Multi Dose Vial Policy (MDVP) statement are met
For multi-dose vials, always use a different new syringe each time to vaccinate

## Slide 13: Question to Participants
Which vial will you use first?
2
1
Expires in 3 weeks
Expires in 2 weeks
Notes: Note to facilitator:
Vial # 1 should be used first. Although the expiry date is later than vial #2, as the status of the VVM has changed, vial #1 should be used first.

## Slide 14: Key Messages
Hexavalent comes in 1-dose (0.5 mL) or 10-dose (5 mL) liquid vaccine vials
Hexavalent 1 and 10-dose vials should be stored between +2° to +8° Celsius. Protect the vaccine from freezing, heat, and exposure to light
Before administering the vaccine, check both the vaccine vial monitor (VVM) and expiry date to ensure the vaccine is still safe for use. The VVM is located on the cap or the label of the vial, depending on the presentation
Once opened, hexavalent 10-dose vial may be kept for use in subsequent immunization sessions for up to 28 days, provided the conditions outlined in the WHO Multi Dose Vial Policy statement are met

## Slide 15: Resources
World Health Organization Multi-Dose Vial Policy (revised 2014): http://apps.who.int/iris/bitstream/10665/135972/1/WHO_IVB_14.07_eng.pdf (Accessed 12 September 2024)
UNICEF Agora: Multi-Dose Vial Policy short e-course: https://agora.unicef.org/course/info.php?id=2065 (Accessed 4 August 2024)
Vaccine Vial Monitor (VVM) training videos: https://vimeo.com/channels/evvm (Accessed 12 September 2024)
World Health Organization and UNICEF: Vaccine vial monitor (VVM) assignments for different WHO-prequalified vaccines and their proper handling https://www.technet-21.org/en/knowledge-hub/main/6785-vaccine-vial-monitor-(vvm)-assignments-for-different-who-prequalified-vaccines-and-their-proper-handling?Itemid=1758 (Accessed 12 September 2024)
WHO. Immunization in Practice: a practical guide for health staff. 2015 update. http://apps.who.int/iris/bitstream/10665/193412/1/9789241549097_eng.pdf (Accessed 12 September 2024)

## Slide 16: Questions to Test Learning
Note to facilitators: See the suggested answers in the notes below
Recognize the vials for the 1 dose and the 10-dose hexavalent vaccine
Describe the correct temperature range for storing hexavalent vaccine
Describe effects of heat exposure on hexavalent vaccine
Understand how to check and interpret the VVM
Understand how to handle hexavalent vaccine after opening the vial
Notes: Recognize the vials for the 1-dose and the 10-dose hexavalent vaccine
Hexavalent vaccine is a ready-to-use, combination injectable vaccine in a liquid formulation
Hexavalent comes in single dose (0.5 mL) or 10-dose (5 mL) liquid vaccine vials
1 dose vials have the VVM in the vial cap and 10-dose vials have the VVM in the label on the side of the vial
Describe the correct temperature range for storing hexavalent vaccine
Hexavalent should be stored between +2° to +8° Celsius. Shelf life at this temperature is 24 months
Liquid vaccines must not be frozen and must be discarded if frozen. If frozen, vaccines lose their potency and provide no protection against disease
Describe effects of heat exposure on hexavalent vaccine
Exposure to too much heat can also reduce the potency of the vaccine
Hexavalent 1 and 10-dose vials will come with Vaccine Vial Monitor (VVM) on the cap and on the vial label, respectively
The VVM records the cumulative heat exposure over time
Understand how to check and interpret the VVM
Before administering the vaccine, you need to check the Vaccine Vial Monitor (VVM) on the vaccine vial cap or label
If the inner square is lighter than the outer circle the vaccine can be used.
If the inner square matches the outer circle, and/or if the inner square is darker than the outer circle – inform your supervisor and discard the vaccine
Understand how to handle hexavalent vaccine after opening the vial
Hexavalent vaccine contains a preservative, allowing 10 dose vials to be opened and kept for use in subsequent immunization sessions for up to 28 days, provided the conditions outlined in the WHO Multi Dose Vial Policy (MDVP) statement are met
For multi-dose vials, always use a different new syringe each time to vaccinate